## Slide 1: Building (Dam Safety) Regulations 2022

## Slide 2: Presentation Overview
Why has the Government introduced the Building (Dam Safety) Regulations 2022?
Building Act 2004 refresh
Key elements of the regulations
Implementation timeline of the regulations.
Key responsibilities for dam owners, Recognised Engineers, and regional authorities.
Visit MBIE’s Building Performance website for more information - https://www.building.govt.nz/managing-buildings/dam-safety/

## Slide 3: Why is the Government doing this work?

## Slide 4
Several significant dam failures in Aotearoa/New Zealand’s history.
Since 1960 there have been 25 dam incidents, with at least 14 that could be considered serious.
Cost of typical dam failure estimated at ~$5.8 million (MWH, 2017).
Aotearoa/New Zealand’s lacks a scheme for assessing and monitoring the safety of dams.
Regulations will bring Aotearoa/New Zealand’s into line with most OECD countries.
The Building Act provides a framework for dam safety management, regulations are needed to bring this into effect.

## Slide 5: A quick Building Act 2004 refresh

## Slide 6
The 1997 Opuha Dam incident, along with the floods of the late 1990s and in 2004, made dam safety a key issue for the building review leading to the Building Act 2004.
The Building Act provides a framework for the regulation of large dams for building control purposes and classifiable dams for post-construction dam safety.
The Regulations bring the framework for post-construction dam safety into full effect.
The Regulations set out responsibilities for dam owners, Recognised Engineers and regional authorities
Large dam means a dam that has a height of 4 or more metres and holds 20,000 or more cubic metres volume of water or other fluid. A building consent is required for work on large dams.
Classifiable dam means a dam that—
  has a height of 4 or more metres and stores 20,000 or more cubic metres volume of water or other fluid.
Classifiable dams are subject to the regulations.
Building Act 2004

## Slide 7: Key steps and implementation timeframes

## Slide 9: Dams impacted by the regulations
Height and volume thresholds:
  A height of 4 or more metres, and stores 20,000 or more cubic metres volume of water, or other fluid.

## Slide 15: Key roles and responsibilities

## Slide 16
Dam owners
    Determine if the water structure meets the definition of a dam.
    Determine if the dam meets the definition of a classifiable dam.
    Notify the regional authority of dam height/reservoir volume and location (only applies to classifiable dams).
    Classify the potential impact of dam failure (low, medium or high classification).
    Have the classification certified by a Recognised Engineer and submit to the regional authority.
    Establish a Dam Safety Assurance Plan (DSAP) for monitoring and maintenance (medium and high only).
    Have the DSAP certified by a Recognised Engineer and submit to the regional authority (medium and high only).
    Prepare an annual dam compliance certificate, have it certified by a Recognised Engineer, and supply it to the regional authority (medium and high only).
    Review the PIC every 5-years. Re-certify and re-submit to regional authority.
    Review the DSAP (medium and high only).
    Notify regional authority of a dangerous dam.

## Slide 17: Recognised Engineers
Under the regulations, Recognised Engineers audit and certify potential impact classification (PIC) and/or dam safety assurance programmes (DSAP).
Engineering New Zealand is responsible for assessing and registering Recognised Engineers.
For more information - https://www.engineeringnz.org/engineer-tools/recognised-engineer-dam-safety/

## Slide 18
Regional Authorities
  Maintain a register of dams in its district.
  Approve or refuse a potential impact classification certificate from a dam owner.
  Approve or refuse a DSAP from a dam owner.
  Receive annual compliance certificate.
  Adopt a dangerous dams, earthquake-prone dams, and flood-prone dams.
  Intervene where a dam is earthquake prone, flood prone or dangerous.

## Slide 19
For more information and resources…
Visit the Building Performance website:
Short video
Infographic/poster
On-line learning module
Guidance document
Prescribed forms templates
Guide - How to measure and calculate dam volume
Resource pack for sector groups
More to come!
https://www.building.govt.nz/managing-buildings/dam-safety/resources/